## Slide 1: Design and Simulation of Multi-tiered Heterogeneous Memory Architecture

## Slide 2: outline
Backgroud and Motivation
Architecture and Design
  Architecture
  Memory Controller
  Data Structure and Algorithm
Evaluation
Conclusion
Notes: Store-nt non-temporal store

## Slide 3: Background
NVM
High storage density
Low cost per byte
Near-zero static power consumption
HBM
High bandwidth
High storage density
Lower power consumption
DRAM
Low storage density
High cost

## Slide 4: Background
Traditional memory architecture：hierarchical architecture and flat architecture
Defects：
  hierarchical architecture：high storage cost and complexity of hardware
  flat architecture：high migration cost

## Slide 5: Motivation
More abundant and multi-layered heterogeneous memory architecture is required
Take advantage of the characteristics of different memory media
There is a lack of simulation platform that can support three or more memory media
Notes: With the demand of big data and high bandwidth applications for memory, more abundant and multi-layered heterogeneous memory architecture is required
Different memory media has different characteristic. It is a great challenge how to make the best memory access performance under the unit cost.
At present, the research of heterogeneous memory architecture is mostly carried out on the simulator, but there is a lack of simulation platform that can support three or more memory media

## Slide 6: outline
Backgroud and Motivation
Architecture and Design
  Architecture
  Memory Controller
  Data Structure and Algorithm
Evaluation
Conclusion
Notes: Store-nt non-temporal store

## Slide 7: Architecture
CPU,TLB and Cache come with GEM5
Hybrid controller is based on GEM5 including four key components
NVM,DRAM, HBM are based on DRAMsim3

## Slide 8: Hybrid controller
Four key parts:
Page Remapping Table
Memory Request Dispatcher
Migration Manager
Page Access Counter
Notes: Manage NVM,DRAM and HBM,including remapping,dispatching,monitoring and migriation

## Slide 9: Remapping Table
check whether a memory request is hit in the remapping table
trigger page migration from NVM to DRAM
update and maintain the remapping table
MemBus
Remapping Table
Dispatcher
Migration
Manager
Bus Req
Bus Req
Bus Resp
Bus Resp
NVM to DRAM Req
Block or Update

## Slide 10: Dispatcher
dispatch memory access requests to different memory media
extract memory access requests to DRAM and sends them to the AC module
Remapping Table
Dispatcher
Migration
Manager
Bus Req
Bus Resp
Access Counter
memroy
HBM
DRAM
NVM
Read/write
Req
Read/write
Resp
Migration
Req
Update
Req

## Slide 11: Access Counter
manage page hotness
pick up the hottest pages according to the counters and trigger page migration from DRAM to HBM
Dispatcher
Migration
Manager
Access Counter
Update
Req
DRAM to HBM
Req

## Slide 12: Migration Manager
receive migration request from Remapping Table and Access Counter
send several read and write packets to the Dispatcher module
Remapping Table
Dispatcher
Migration
Manager
DRAM to HBM
Req
Access Counter
Migration
Req
NVM to DRAM Req
Block or Update

## Slide 13: Remapping Table
NVM-to-DRAM address mapping: the first column is NVM page, the second column is DRAM page, the third column is empty
NVM-to-HBM address mapping: the first column is NVM page, the second column is HBM page, the third column is DRAM
NVM Page | Page No. of Cache Hit (DRAM or HBM) | Page No. After Migration (DRAM or HBM)
0x0001 | 0x1000 | 
0x0002 | 0x1001 | 
0x0003 | 0x2000 | 0x1002
…… | …… | ……

## Slide 14: Hot Page Monitoring Mechanism
efficient to track hot pages
significantly reducing the hardware cost

## Slide 15: outline
Backgroud and Motivation
Architecture and Design
  Architecture
  Memory Controller
  Data Structure and Algorithm
Evaluation
Conclusion
Notes: Store-nt non-temporal store

## Slide 16: Evaluation
Simulator :
GEM5+DRAMsim3
Five memory systems :
A pure NVM system: 4 GB NVM,
A pure DRAM system: 4 GB DRAM
A pure HBM system: 4 GB HBM,
A flat heterogeneous memory system : 4 GB DRAM and 256 MB HBM
Multi-tier heterogeneous memory system : 4 GB NVM main memory, 1 GB DRAM, and 256 MB HBM cache
Workload :
Standard Performance Evaluation Corporation CPU2017 (SPEC CPU2017)

## Slide 17: Evaluation Results
IPC of applications in a multi-core scenario
Our system can improve the performance of gcc_r and x264_r by about 2.5× and 4.4× compared with the pure NVM system, respectively.
Our system can also improve the performance of x264_r by 57.4% compared with the pure DRAM system, and the performance gap between the pure HBM system is even less than 10%.

## Slide 18: Evaluation results
Application IPC using MEA algorithm and full counters
The performance gap between MEA and full-counter algorithms is less than 1%.
MEA offers rather high accuracy for hot page monitoring, while significantly reducing the hardware overhead.

## Slide 19: Evaluation results
Application IPCs using different replacement algorithms
The combination of our random replacement algorithm and MEA-based hot page monitoring algorithm can achieve similar performance compared with the pure HBM system.

## Slide 20: outline
Backgroud and Motivation
Architecture and Design
  Architecture
  Memory Controller
  Data Structure and Algorithm
Evaluation
Conclusion
Notes: Store-nt non-temporal store

## Slide 21: Conclusion
We design a multi-tier heterogeneous memory architecture.
  composed of NVM, DRAM, and HBM
  design a MEA-based hot page monitor algorithm
  a random HBM page replacement algorithm
  implement it based on GEM5 and DRAMsim3 simulators
Our multi-tiered hybrid memory architecture significantly improves application performance.
  improve application performance by an average of 2.5× compared with an NVM-only architecture, and up to 57.4% compared with a DRAM-only architecture
  the performance gap between our architecture and a HBM-only architecture is less than 10%

## Slide 22
Thank you
&
Questions?